## Slide 1
DIGITAL LOGIC DESIGN
Design and Simulation of a 4-Bit Binary Arithmetic Calculator
A compact digital system that accepts two 4-bit binary numbers and performs arithmetic operations using combinational logic.
KEY IDEA
Binary inputs → Arithmetic logic → Binary result
4-BIT RANGE
0000₂ to 1111₂ | 0 to 15₁₀
CIRCUIT VIEW
4-BIT ARITHMETIC
0101 + 0011
0
1
0
1
1
0
1
0
RESULT = 1000₂

## Slide 2
1. Introduction, Need & Objectives
Why a 4-bit arithmetic calculator is useful in digital logic
INTRODUCTION
Digital systems represent numbers using binary bits. A 4-bit arithmetic calculator demonstrates how simple logic gates can be combined to perform useful numerical operations.
OBJECTIVES
• Take two 4-bit inputs A and B. • Select an arithmetic operation. • Generate a 4-bit result. • Monitor carry-out or borrow/overflow. • Verify the circuit using simulation and test cases.
DESIGN REQUIREMENT
The circuit should be modular, easy to test, and expandable to larger bit widths.
CIRCUIT VIEW
A[3:0]
B[3:0]
CONTOLR
4-BIT ADDER
RESULT

## Slide 3
2. Circuit Design & Working Principle
The calculator is built from full adders, XOR logic and control signals
MAIN COMPONENTS
1. INPUT REGISTERS
A[3:0] and B[3:0] hold the two binary operands.
2. OPERATION CONTROL
A control bit selects addition or subtraction.
3. ADDER / SUBTRACTOR
Four full-adder stages process one bit at a time.
4. OUTPUT & STATUS
R[3:0] gives the result; COUT indicates final carry.
SUBTRACTION PRINCIPLE
A − B = A + (~B) + 1
CIRCUIT VIEW
FA0
SUM CARRY
FA1
SUM CARRY
FA2
SUM CARRY
FA3
SUM CARRY
C₀
C₄

## Slide 4
3. Simulation, Test Cases & Example
Simulation confirms that the logic produces the expected binary result
EXAMPLE 1 — ADDITION
A = 0101₂ = 5₁₀ B = 0011₂ = 3₁₀
0101 +0011 ───── 1000
Therefore: 5 + 3 = 8 Result = 1000₂
EXAMPLE 2 — SUBTRACTION
0110₂ − 0010₂ = 0100₂ (6 − 2 = 4)
TESTING CHECKLIST
Normal result • zero • carry • subtraction
CIRCUIT VIEW
A3
A2
B1
R0
TIME →

## Slide 5
4. Results, Applications & Conclusion
What the completed design demonstrates
RESULTS
✓ Correctly processes two 4-bit operands ✓ Supports addition and subtraction logic ✓ Produces a 4-bit binary output ✓ Carry/borrow behavior can be observed ✓ Simulation makes errors easy to identify
APPLICATIONS
• Arithmetic Logic Units (ALUs) • Digital calculators and counters • Microprocessor datapaths • Embedded digital systems • Digital electronics laboratories
CONCLUSION
The 4-bit calculator shows how basic combinational blocks can be integrated into a practical arithmetic system.
CIRCUIT VIEW
4-BIT ARITHMETIC
0101 + 0011
0
1
0
1
1
0
1
0
RESULT = 1000₂